## Slide 1
Inventory Reorder Protocol: when and how to reorder
Learning goal for junior stockroom coordinators | All data are synthetic
LEARNING GOAL
Apply one simple reorder-point rule to decide, every day, whether to place a restocking order.
We explain the logic, work through one example, then give a short practice exercise. The answer is revealed on the slide after the exercise.
Outcome: from three counts (on-hand, on-order, committed) and one trigger, you can state ORDER or WAIT and show the arithmetic.
Slide | Topic | What you will do
2 | Rule | Learn the two formulas and the trigger
3 | Worked example | Calculate a reorder point with units
4 | Inventory | Compute inventory position; decide
5 | Process | Follow the daily decision loop
6 | Practice | Decide ORDER or WAIT yourself
7 | Misconceptions | Check the answer; avoid three errors
8 | Checklist | Verify before ordering

## Slide 2
The rule: compare inventory position with the reorder point
Two formulas and one decision, applied at every daily review
1 REORDER POINT (the trigger)
Reorder point = daily demand × lead time (days) + safety stock
2 INVENTORY POSITION
Inventory position = on-hand + on-order − committed
3 DECISION
If inventory position ≤ reorder point → ORDER.
Otherwise → WAIT.
Units: demand in units/day, lead time in days, all stock in units. Convert everything to units before comparing.
Term | Meaning (unit)
Daily demand | Average units used per day (units/day)
Lead time | Days from placing an order to receipt (days)
Safety stock | Buffer for demand or delay surprises (units)
On-hand | Units physically in the stockroom (units)
On-order | Units ordered, not yet received (units)
Committed | Units promised to jobs, not yet issued (units)

## Slide 3
Worked example: the reorder point is 134 units
18 units/day × 6 days = 108 units of lead-time demand; + 26 units safety stock = 134 units
18 units/day
Daily demand
6 days
Lead time
26 units
Safety stock
134 units
Reorder point (result)
Step | Calculation | Result | Unit logic
1 Lead-time demand | 18 units/day × 6 days | 108 units | days cancel, leaving units
2 Add safety stock | 108 units + 26 units | 134 units | units + units = units
3 Set the trigger | Reorder point | 134 units | compare inventory position with 134
Cumulative units needed over the 6-day lead time
Chart: 
| Day 1 | Day 2 | Day 3 | Day 4 | Day 5 | Day 6
Lead-time demand (units) | 18 | 36 | 54 | 72 | 90 | 108
Demand + safety stock (units) | 44 | 62 | 80 | 98 | 116 | 134
Result: when inventory position falls to 134 units or fewer, place an order.

## Slide 4
Inventory position is 129 units, below the 134 trigger: ORDER
105
On-order and committed units stay in the calculation; on-hand alone is never compared
Line | Units | Arithmetic
On-hand | 126 | + (in stockroom)
On-order | 20 | + (not yet received)
Committed | 17 | − (promised to jobs)
Inventory position | 129 | 126 + 20 − 17 = 129
Reorder point | 134 | trigger: 129 ≤ 134 → ORDER
Target position | 234 | order up to this level
Order quantity | 105 | 234 − 129 = 105
Inventory position vs. trigger and target (units)
Chart: 
| Inventory position | Reorder point | Target position
Before order | 129 | 134 | 234
After placing 105-unit order | 234 | 134 | 234
DECISION: 129 ≤ 134 → ORDER. Order quantity = 234 − 129 = 105 units. Keep on-order (20) and committed (17) in the position.

## Slide 5
Daily process: read, calculate, compare, then ORDER or WAIT
The WAIT branch loops back to the next daily review
1
Read counts
2
Calculate inventory position
3
Compare with reorder point
ORDER
position ≤ reorder point
WAIT
position > reorder point
WAIT returns to the next daily review
1 Read counts | 2 Calculate position | 3 Compare | Act
On-hand, on-order, committed (units) | On-hand + on-order − committed | Is position ≤ reorder point? | Yes: ORDER up to target. No: WAIT

## Slide 6
Practice: should you ORDER or WAIT?
Work it out on paper first; the answer is revealed on the next slide
Given | Value
Inventory position | 146 units
Reorder point | 134 units
Rule | ORDER if position ≤ reorder point
Step | Your work
1 Compare position with trigger | 146 ____ 134 (≤ or >)
2 Difference from trigger | 146 − 134 = ____ units
3 Decision | ORDER / WAIT
HINTS
• Use inventory position, not on-hand.
• Write ≤ or > between the two numbers before deciding.
• If the position is above the trigger, state how many units above.

## Slide 7
Practice answer: WAIT. Then avoid three common errors
146 > 134: the position is 12 units above the trigger
ANSWER: WAIT. 146 > 134, and 146 − 134 = 12 units above the reorder point. Re-check at the next daily review.
Position vs. reorder point (units)
Chart: 
| Worked example (ORDER) | Practice (WAIT)
Inventory position | 129 | 146
Reorder point | 134 | 134
Misconception | Why it is wrong | Do this instead
Compare on-hand alone with the trigger | Ignores units on order and units already committed | Compare inventory position = on-hand + on-order − committed
Multiply safety stock by lead time | Safety stock is a fixed buffer in units | Add it once: demand × lead time + safety stock
Treat a larger reorder point as the order quantity | The reorder point is a trigger, not the order quantity | Order quantity = target − position (234 − 129 = 105)

## Slide 8
Checklist before ordering: verify, include, subtract, then check
Number line of the example: position 129 sits in the ORDER zone; order up to 234
ORDER zone
WAIT zone (above 134)
120
150
180
210
240 units
Reorder point 134
Target position 234
Example 129
→ ORDER
Practice 146
→ WAIT
Order quantity 105 = 234 − 129
Check | What to do | Example arithmetic
1 Verify units | All stock in units; demand in units/day; lead time in days | 18 units/day × 6 days = 108 units
2 Include existing orders | Add on-order units to on-hand | 126 + 20 = 146 units
3 Subtract commitments | Subtract committed units | 146 − 17 = 129 units
4 Check the trigger | ORDER only if position ≤ reorder point | 129 ≤ 134 → ORDER 105 units