## Slide 1
Reorder Point: Knowing When to Order
A field guide for new stockroom staff
YOUR LEARNING GOAL
Learn one simple reorder-point rule that tells you when to reorder a stock item, and apply it correctly on every shift.
You will see the logic, a worked example, and a short practice exercise with its answer.
1
Understand the logic
Reorder point, inventory position and the trigger comparison.
2
Follow a worked example
Every arithmetic step shown, with units labeled.
3
Try a practice exercise
Decide ORDER or WAIT; the answer is revealed on the following slide.
All figures in this guide are synthetic training data.

## Slide 2
The Rule in Three Parts
Two numbers to calculate, one comparison to make
1 · REORDER POINT (the trigger)
Reorder point = daily demand × lead time in days + safety stock
Units: (units/day × days) = units, then add safety stock in units.
2 · INVENTORY POSITION (what you really have)
Inventory position = on-hand + on-order − committed
Count stock on the shelf, add stock already ordered, subtract stock already promised.
3 · THE DECISION
If inventory position ≤ reorder point → place an ORDER. Otherwise → WAIT.
Always compare the inventory position, not on-hand alone, with the reorder point.

## Slide 3
Worked Example: Finding the Reorder Point
Every step shown, every number labeled with its unit
GIVEN
Input | Value | Unit
Daily demand | 19 | units/day
Lead time | 5 | days
Safety stock | 28 | units
RESULT
Reorder point = 123 units
This is the trigger, not an order quantity.
STEP 1 · Lead-time demand (used while you wait)
19 units/day × 5 days = 95 units
STEP 2 · Add safety stock once (buffer)
95 units + 28 units = 123 units
STEP 3 · Read the trigger
Order when inventory position ≤ 123 units
Units check: units/day × days = units, so every term is in units before you add them.

## Slide 4
Checking Inventory: Order or Wait?
Inventory position 118 is below the reorder point of 123, so we ORDER 105 units
STEP 1 · Inventory position
115 on-hand + 20 on-order − 17 committed = 118 units
STEP 2 · Compare with the reorder point
118 ≤ 123 units → ORDER
STEP 3 · Order quantity
223 target − 118 position = 105 units
Position vs. trigger and target (units)
Chart: 
| Inventory position | Reorder point | Target position
Units | 118 | 123 | 223
Gap to target: 223 − 118 = 105 units to order
Keep the 20 on-order and 17 committed units in the count; never drop them from the position.

## Slide 5
The Daily Decision Path
Follow the same steps for each item at every daily review
1 · Read counts
on-hand, on-order, committed
2 · Calculate inventory position
on-hand + on-order − committed
3 · Compare with reorder point
Is position ≤ trigger?
ORDER
position at or below the trigger
WAIT
position above the trigger
WAIT branch → return to step 1 at the next daily review
Example from the previous slide: position 118 ≤ reorder point 123 → ORDER 105 units.

## Slide 6
Practice: Your Turn
Apply the rule to one item, then check your answer on the next slide
135 units
Inventory position
123 units
Reorder point (trigger)
THE QUESTION
Using the rule, should you ORDER or WAIT? Write the comparison and your decision.
Your work
Comparison
135 ____ 123
Decision
Answer revealed on the next slide.

## Slide 7
Answer and Common Misconceptions
First, the practice answer, then three mistakes to avoid
Practice answer: WAIT
135 units > 123 units. The position is 12 units above the trigger (135 − 123 = 12), so no order yet.
On-hand alone
Do not compare on-hand alone with the trigger. Use on-hand + on-order − committed.
Safety stock × lead time
Do not multiply safety stock by lead time. Only daily demand is multiplied; safety stock is added once.
Trigger ≠ quantity
A larger reorder point is a trigger, not the order quantity. It tells you when, not how much.
Each of these mistakes can flip the ORDER / WAIT decision. Check them every time.

## Slide 8
Pre-Order Checklist
Four checks before you place any order
1 · Verify units: every number uses the same unit of measure.
2 · Include existing orders: add the on-order quantity.
3 · Subtract commitments: remove units already promised.
4 · Then check the trigger: ORDER only if position ≤ reorder point.
Where does the position sit?
At or left of the trigger: ORDER. Right of it: WAIT.
ORDER zone (≤ 123)
WAIT zone (> 123)
Reorder point 123
118
example: ORDER
135
practice: WAIT
Inventory position (units), scale 110 to 140
Run all four checks on every shift before placing an order.